LISA Noise Curves - Consider Cornish and Robson arXiv 1803.01944v1 and Maggiore Chapter7
Bill Gabella
20180410
Refs:
Maggiore, Gravitational Waves, Chapter 7
Cornish and Robson, The construction and use of LISA sensitivity curves,
arXiv 1803.01944v1

---
Some Points about our Exops
- Exop GW frequencies are low compared to either the round-trip time in a LISA arm (16.7 s) as a frequency, 60 mHz, or compared to f_star = c/(2pi L) which is 19.1 mHz.
- Highest Exop GW frequency, see histogram in PrettyPlotsGWStrainEtc notebook, is XXXX
- This puts us in the “LIGO Limit” where the LISA “signal response function of the instrument” (sky and polarization averaged) is the same at LIGO, \cal R = 1/5 per channel.
- Oh yeah, C&R say that there are two independent Michelson interferometer channels below f_star and three above f_star.
- So you can multiply signal, usual \cal R, by 2 or 3.
- That is Sky and Polarization averaged.

---
Links
Cornish and Robson, https://arxiv.org/abs/1803.01944
aa

---
Backup

---
Gravitational Wave Spectrum

---
Strain from Exoplanets
WRONG!!
from 2016 work
Exop PSR J1719-1438,
“Diamond Planet”
WRONG!!
[Speaker Notes: http://www.ast.cam.ac.uk/~cjm96/noise_curve.pdf]